## Slide 2: Memory Definitions
Memory ─ kumpulan sel penyimpanan bersama dengan sirkuit yang diperlukan untuk mentransfer informasi ke dan dari sel tersebut.
Memory Organization ─ struktur arsitektur dasar memori dalam hal bagaimana data diakses.
Random Access Memory (RAM) ─ memori yang diatur sedemikian rupa sehingga data dapat ditransfer ke atau dari sel mana pun (atau kumpulan sel) dalam waktu yang tidak bergantung pada sel tertentu yang dipilih.
Memory Address ─ Sebuah vektor bit yang mengidentifikasi elemen memori tertentu (atau kumpulan elemen).

## Slide 3: Memory Definitions (Continued)
Typical data elements are:
  bit ─ satu digit biner
  byte ─ kumpulan delapan bit yang diakses bersama-sama
  word ─ kumpulan bit biner yang ukurannya merupakan unit akses khas untuk memori. Biasanya merupakan pangkat dua kelipatan byte (misalnya, 1 byte, 2 byte, 4 byte, 8 byte (64 bit), dll.)
Memory Data ─ Sebuah bit atau kumpulan bit untuk disimpan atau diakses dari sel memori.
Memory Operations ─ operasi pada data memori yang didukung oleh unit memori. umumnya, operasi read dan write pada beberapa elemen data (bit, byte, word, etc.).
Notes: "word" merujuk pada unit data dasar yang dapat diakses oleh prosesor atau unit pemrosesan komputer dalam satu operasi.

## Slide 4: Memory Organization
Sering sekali diatur sesuai kebutuhan arsitektur komputer tertentu.
  Digital Equipment Corporation PDP-8 – used a 12-bit address to address 4096 (2^12) 12-bit words.
  IBM 360 – used a 24-bit address to address 16,777,216 8-bit bytes, or 4,194,304 32-bit words.
  Intel 8080 – (8-bit predecessor to the 8086 and the current Intel processors) used a 16-bit address to address 65,536 8-bit bytes.

## Slide 5: Memory Block Diagram
A basic memory system is shown here:
k address lines are decoded to address 2k words of memory.
Each word is n bits.
Read and Write are single control lines defining the simplest of memory operations.
n Data Input Lines
k Address Lines
Read
Write
n Data Output Lines
Memory
Unit
2k Words
n Bits per Word
k
1
1
n
n

## Slide 6: Memory Organization Example
Example memory contents:
  A memory with 3 address bits & 8 data bits has:
  k = 3 (address line) and n = 8 (data input line) so 23 = 8 addresses labeled 0 to 7.
  23 = 8 words of 8-bit data
Memory Address
Binary Decimal
Memory
Content
0 0 0 0
1 0 0 0 1 1 1 1
0 0 1 1
1 1 1 1 1 1 1 1
0 1 0 2
1 0 1 1 0 0 0 1
0 1 1 3
0 0 0 0 0 0 0 0
1 0 0 4
1 0 1 1 1 0 0 1
1 0 1 5
1 0 0 0 0 1 1 0
1
1 0 6
0 0 1 1 0 0 1 1
1 1 1 7
1 1 0 0 1 1 0 0

## Slide 7: Basic Memory Operations
Memory operations require the following:
  Data ─ data written to, or read from, memory as required by the operation.
  Address ─ specifies the memory location to operate on. The address lines carry this information into the memory. Typically: n bits specify locations of 2n words.
  An operation ─ Information sent to the memory and interpreted as control information which specifies the type of operation to be performed. Typical operations are READ and WRITE. Others are READ followed by WRITE and a variety of operations associated with delivering blocks of data. Operation signals may also specify timing info.

## Slide 8: Basic Memory Operations (continued)
Read Memory ─ an operation that reads a data value stored in memory:
  Place a valid address on the address lines.
  Wait for the read data to become stable.
Write Memory ─ an operation that writes a data value to memory:
  Place a valid address on the address lines and valid data on the data lines.
  Toggle the memory write control line
Sometimes the read or write enable line is defined as a clock with precise timing information (e.g. Read Clock, Write Strobe).
  Otherwise, it is just an interface signal.
  Sometimes memory must acknowledge that it has completed the operation.
Notes: Toggle: alihkan

## Slide 9: Memory Operation Timing
Most basic memories are asynchronous
  Storage in latches or storage of electrical charge
  No clock
Controlled by control inputs and address
Timing of signal changes and data observation is critical to the operation
Read timing:
Read cycle
Clock
Address
Memory
enable
Read/
Write
Data
output
20 ns
T1
T2
T3
T4
T1
Address valid
65 ns
Data valid
Notes: 1 detik = 1,000,000,000 nanosecond

## Slide 10: Memory Operation Timing
Write timing:
Critical times measured with respect to edges of write pulse (1-0-1):
  Address must be established at least a specified time before 1-0 and held for at least a specified time after 0-1 to avoid disturbing stored contents of other addresses
  Data must be established at least a specified time before 0-1 and held for at least a specified time after 0-1 to write correctly
Write cycle
Clock
Address
Memory
enable
Read/
Write
Data
input
20 ns
T1
T2
T3
T4
T1
Address valid
Data valid
75 ns

## Slide 11: RAM Integrated Circuits
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges (muatan listrik) on capacitors
    Charge “leaks” off
    Periodic refresh of charge required
Dependence on Power Supply
  Volatile – loses (hilang) stored information when power turned off
  Non-volatile – retains (menahan) information when power turned off

## Slide 12: Static RAM  Cell
Array of storage cells used to implement static RAM
Storage Cell
  SR (set reset) Latch
  Select input for control
  Dual Rail Data Inputs B and B
  Dual Rail Data Outputs C and C
Select
B
RAM cell
C
C
B
S
R
Q
Q
Notes: Gerbang Logika AND
Set-Reset latch:
Jika sinyal Set (S) diaktifkan (1), itu mengakibatkan output Q menjadi 1.
Jika sinyal Reset (R) diaktifkan (1), itu mengakibatkan output Q menjadi 0.

## Slide 13: Static RAM  Bit Slice
Represents all circuitry that is required for 2n 1-bit words
  Multiple RAM cells
  Control Lines:
    Word select i – one for each word
    Bit Select
  Data Lines:
    Data in
    Data out
(a) Logic diagram
Select
S
R
Q
Q
B
RAM cell
C
C
B
Select
S
R
Q
Q
RAM cell
X
Word
select
0
Word
select
2
n
 1
Data in
Write logic
Read/
Write
Bit
select
S
R
Q
Q
X
X
X
Word
select
0
Word
select
1
Word
select
2
n
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
(b) Symbol
RAM cell
RAM cell
RAM cell
Data out
Read logic
 1

## Slide 14: 2n-Word  1-Bit RAM IC
Read/
To build a RAM IC from a RAM slice, we need:
  Decoder  decodes the n address lines to 2n word select lines
  A 3-state buffer 
  on the data output permits RAM ICs to be combined into a RAM with c  2n words
Word select
Read/Write
logic
Data in
Data out
Write
Bit
select
(b) Block diagram
RAM cell
RAM cel
l
RAM cell
Data input
Chip select
Read/Write
Data
output
A
3
A
2
A
1
A
0
2
3
2
2
2
1
2
0
4-to-16
Decoder
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
3
A
2
A
1
A
0
Data
input
Data
output
(a) Symbol
Read/
Write
Memory
enable
16 x
1
RAM

## Slide 15: Dynamic RAM (DRAM)
Basic Principle: Storage of information on capacitors.
Charge and discharge of capacitor to change stored value
Use of transistor as “switch” to:
  Store charge
  Charge or discharge
See next slide for circuit, hydraulic analogy, and logical model.

## Slide 16: Dynamic RAM (continued)
(a)
(c)
Select
D
C
Q
B
DRAM cell
model
C
(f)
(g)
(h)
Select
B
T
C
DRAM cell
To Pump
(b)
(d)
(e)
Stored 1
Stored 0
Write 1
Write 0
Read 1
Read 0
Notes: Warning: (d), (e), (f), and (g) are animated. Each animation is triggered with a mouse click
and goes through two steps at 1 second intervals.

## Slide 17: Dynamic RAM - Bit Slice
C is driven by 3-state drivers
Sense amplifier is used to change the small voltage change on C into H or L
In the electronics, B, C, and the sense amplifier output are connected to make destructive read into non-destructive read
Data in
(b) Symbol
(a) Logic diagram
Select
B
Select
Word
select
0
Word
select
2
n
2
1
Write logic
Bit
select
Data out
Read logic
D
C
Q
DRAM cell
model
D
C
Q
DRAM cell
model
C
Sense
amplifier
Read/Write
logic
Data in
Data out
Bit
select
DRAM cell
DRAM cell
DRAM cell
Word
select
0
Word
select
1
Word
select
2
n
2
1
Read/
Write
Read/
Write

## Slide 18: Dynamic RAM Read Timing
Read cycle
20 ns
T1
T2
T3
T4
T1
Data valid
65 ns
Hi-Z
Read/
Write
Data
output
Clock
Row
Address
Column
Address
RAS
CAS
Address
Output
enable

## Slide 19: Soal:
Berapa banyak saluran (line) address yang diperlukan untuk sejumlah lokasi berikut ini
a. 1.024 lokasi
b. 8.192 lokasi
c. 65.536 lokasi
2. Berapa banyak lokasi memory dan berapa kapasitas memory untuk konfigurasi RAM berikut ini :
a. 2K x 1
b. 8K x 8
c. 4K x 8
d. 8K x 4

## Slide 20: Terimakasih